## Slide 1
Lecture 7
Combinational Circuits -
MSI Circuits
Department of Computer Science and Engineering, BRAC University
CSE260 : Digital Logic Design

## Slide 2
2
The design of combinational circuits starts from the verbal outline of the problem and ends in a logic circuit diagram
Design Procedure
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 3
3
The procedure involves the following steps:
Design Procedure:
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
6. The logic diagram is drawn
2. Input and Output variables are determined
5. The simplified boolean function for each output is obtained
3. Letter symbols are assigned to the input and output variables
1. The problem is stated
4. Truth table that defines relationship between input and outputs is derived.
Hint: Aren’t these the steps used for solving car-garage alarm system? So we are familiar with combinational circuit design!

## Slide 4
4
Different combinational circuit design methods:
  Gate-level method (with logic gates)
  Block-level design method
Design methods make use of logic gates and useful functional blocks.
  These are available as Integrated Circuit (IC) chips.
Design Methods
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 5
5
Why is it better to use IC than classical gate method?
IC consists of gates all packed up together internally, which keeps the gates safe inside as well as makes it economical by reducing external interconnection wires
As number of input increase, making the truth table and k-map gets cumbersome
Design Methods
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 6
6
Type of IC chips (based on packing density) :
Design Methods
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
Small-scale integration (SSI) | up to 12 gates
Medium-scale integration (MSI) | 12 - 99 gates
Large-scale integration (LSI) | 100 - 9999 gates
Very large-scale integration (VLSI) | 10,000 - 99,999 gates
Ultra large-scale integration (ULSI) | > 100,000 gates

## Slide 7
7
Main objectives of circuit design:
  (i) reduce cost
    reduce number of gates (for SSI circuits)
    reduce IC packages (for complex circuits)
  (ii) increase speed
  (iii) design simplicity (reuse blocks where possible)
Design Methods
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 8
8
More complex circuits can be built using block-level method.
In general, block-level design method (as opposed to gate-level design) relies on algorithms or formulae of the circuit, which are obtained by decomposing the main problem to sub-problems recursively (until small enough to be directly solved by blocks of circuits).
Block-Level Design Method
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 9
9
Four common and useful MSI circuits are:
  Decoder
  Demultiplexer
  Encoder
  Multiplexer
Block-level outlines of MSI circuits:
Useful MSI circuits
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 10
10
Convert binary information from n input lines to (max. of) 2n output lines.
Known as n-to-m-line decoder, or simply n:m or n×m decoder (m ≤ 2n).
May be used to generate 2n (or fewer) minterms of n input variables.
Decoders
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 11
11
From truth table, circuit for 2×4 decoder is:
Note: Each output is a 2-variable minterm (X'Y', X'Y, XY' or XY)
Decoders
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
2x4
Dec
2-bit code
X
Y
F0 F1 F2 F3
Bulb 0
Bulb 1
Bulb 2
Bulb 3
X | Y | F0 | F1 | F2 | F3
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1

## Slide 12
12
Design a 3×8 decoder by yourself.
Decoders
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 13
13
Solution:
Decoders
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
x | y | z | F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 14
14
In general, for an n-bit code, a decoder could select up to 2n lines:
Decoders
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
:
:
n-bit
code
n to 2n
decoder
up to 2n
output lines
As n input generates 2^n output, which reminds us of canonical SOP, thus a decoder can be used to generate any function

## Slide 15
15
Example 1: Full adder circuit with decoder (3 x 8 decoder)
We know,
S(x,y,z) = ∑(1,2,4,7)
C(x,y,z) = ∑(3,5,6,7)
Decoders
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 16
16
Given an input line and a set of selection lines, the demultiplexer will direct data from input to a selected output line.
An example of a 1-to-4 demultiplexer:
Demultiplexer
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
S1 | S2 | Y0 | Y1 | Y2 | Y3
0 | 0 | D | 0 | 0 | 0
0 | 1 | 0 | D | 0 | 0
1 | 0 | 0 | 0 | D | 0
1 | 1 | 0 | 0 | 0 | D
demux
Data D
Outputs
select
S1 S0
Y0 = D.S1'.S0'
Y1 = D.S1'.S0
Y2 = D.S1.S0'
Y3 = D.S1.S0

## Slide 17
17
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 18
18
The demultiplexer is actually identical to a decoder with enable. A decoder with an enable input can function as a demultiplexer (or demux) Decoder + enable= demultiplexer
The selection of a specific output line is controlled by the bit values of ‘n’-selection lines.
Demultiplexer
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
2x4 Decoder
D
S1
S0
Y0 = D.S1'.S0'
Y1 = D.S1'.S0
Y2 = D.S1.S0'
Y3 = D.S1.S0
E
demux
Data D
Outputs
select
S1 S0
Y0
Y1
Y2
Y3

## Slide 19
19
4-line-to-16 line Decoder constructed with two 3-line-to-8 line decoders with enables
Decoder (More Applications)
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 20
20
4-line-to-16 line Decoder constructed with two 3-line-to-8 line decoders with enables
When w=0, the top decoder is enabled and the other is disabled. The bottom decoder outputs are all 0’s , and the top eight outputs generate min-terms 0000 to 0111.
When w=1, the enable conditions are reversed. The bottom decoder outputs generate min-terms 1000 to 1111, while the outputs of the top decoder are all 0’s.
Decoder
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
W | X | Y | Z
0 | 0 | 0 | 0
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
1 | 1 | 1 | 1

## Slide 21
21
F(a,b,c,d)=∑(0,1,3,5,12,13)
Implement the above boolean
function using
a. 3:8 Decoder(s).
b. 2:4 Decoder(s).
Decoder
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 22
22
F(a,b,c,d)=∑(0,1,3,5,12,13)
Implement the above boolean
function using
a. 3:8 Decoder(s).
b. 2:4 Decoder(s).
Decoder
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 23
23
A multiplexer is a device which has
(i) a number of input lines
(ii) a number of selection lines
(iii) one output line
A Multiplexer steers one of 2n inputs to a single output line, using n selection lines. Also known as a data selector.
Multiplexer
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
2n:1
Multiplexer
output
inputs
:
select
...

## Slide 24
24
Truth table for a 4-to-1 multiplexer:
Multiplexer
Department of Computer Science and Engineering
I0 | I1 | I2 | I3 | S1 | S0 | Y
d0 | d1 | d2 | d3 | 0 | 0 | d0
d0 | d1 | d2 | d3 | 0 | 1 | d1
d0 | d1 | d2 | d3 | 1 | 0 | d2
d0 | d1 | d2 | d3 | 1 | 1 | d3
CSE260 - Digital Logic Design
S1 | S0 | Y
0 | 0 | I0
0 | 1 | I1
1 | 0 | I2
1 | 1 | I3

## Slide 25
25
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 26
26
Output of multiplexer is
“sum of the (product of data lines and selection lines)”
Often known as Data selector as it selects one of the many inputs and steers the binary information to the output line.
Example: the output of a 4-to-1 multiplexer is:
Y = I0.(S1’.S0') + I1.(S1’.S0) + I2.(S1.S0') + I3.(S1.S0)
Multiplexer
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 27
27
Draw the internal circuit diagram (logic diagram) of a 4-to-1 multiplexer.
Solution: Y = I0.(S1’.S0') + I1.(S1’.S0) + I2.(S1.S0') + I3.(S1.S0)
Try it yourself
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
S1 | S0 | Y
0 | 0 | d0
0 | 1 | d1
1 | 0 | d2
1 | 1 | d3
(a) Logic Diagram
(b) Function Table
(c) Block Diagram

## Slide 28
28
Larger multiplexers can be constructed from smaller ones.
An 8-to-1 multiplexer can be constructed from smaller multiplexers like this (from two 4x1 and one 2x1):
Larger Multiplexers
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
S2 | S1 | S0 | Y
0 | 0 | 0 | I0
0 | 0 | 1 | I1
0 | 1 | 0 | I2
0 | 1 | 1 | I3
1 | 0 | 0 | I4
1 | 0 | 1 | I5
1 | 1 | 0 | I6
1 | 1 | 1 | I7

## Slide 29
29
Another implementation of an 8-to-1 multiplexer using smaller multiplexers (four 2x1 and one 4x1):
Larger Multiplexers
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
S2 | S1 | S0 | Y
0 | 0 | 0 | I0
0 | 0 | 1 | I1
0 | 1 | 0 | I2
0 | 1 | 1 | I3
1 | 0 | 0 | I4
1 | 0 | 1 | I5
1 | 1 | 0 | I6
1 | 1 | 1 | I7
Q: Can we use only 2:1 multiplexers?

## Slide 30
30
Q: Can we use only
2:1 multiplexers?
Larger Multiplexers
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 31
31
Q: A 16-to-1 multiplexer can be constructed from only 4-to-1 multiplexers:
Try it yourself: Larger Multiplexers
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 32
32
Encoder is a digital function that produces a reverse operation of a decoder!
It has 2n input lines and n output lines
Encoder
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 33
33
X = D4 + D5 + D6 + D7
Y = D2 + D3 + D6 + D7
Z = D1 + D3 + D5 + D7
Example: Octal-binary encoder
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7 | x | y | z
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1

## Slide 34
34
X = D4 + D5 + D6 + D7
Example: Octal-binary encoder
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
Z = D1 + D3 + D5 + D7
Y = D2 + D3 + D6 + D7
Octal to Binary Encoder Logic Diagram
There are 8 input variables so there will be 256 input combination, amongst which in Octal-binary encoder only 8 are useful

## Slide 35
35
Accepts multiple values and encodes them
  Works when more than one input is active
Consists of:
  Inputs (2n)
  Outputs
    when more than one output is active, sets output to correspond to highest input
    V (indicates whether any of the inputs are active). This helps to show the output when all inputs are 0s
  Selectors / Enable
Priority Encoder
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 36
36
Design a priority encoder, which will allow more than one input to exist and encodes only the highest priority input line. For example, 8x3 encoder in a if user give D2 and D7 together, it will allow data of D7 to pass.
Example: Priority Encoder
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 37
37
Design a priority encoder, which will allow more than one input to exist and encodes only the highest priority input line. For example, 4x2 encoder in a if user give D2 and D3 together, it will allow data of D3 to pass.
Example: 4x2 Priority Encoder
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 38
38
Designing a 4x2 priority encoder
Example: 4x2 Priority Encoder
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
D3 | D2 | D1 | D0 | A1 | A0 | V
0 | 0 | 0 | 0 | X | X | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
Note: Amongst all 3 input, D2 is highest so output reflects the binary value of 2
Note: V is not really an output, just shows whether there is an active input or not.
From the truth table
A1 = ∑(4,5,6,7,8,9,10,11,12,13,14,15) + d(0)
A0 = ∑(2,3,8,9,10,11,12,13,14,15) + d(0)

## Slide 39
39
Example: 4x2 Priority Encoder
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
A1 = ∑(4,5,6,7,8,9,10,11,12,13,14,15) + d(0)
A0 = ∑(2,3,8,9,10,11,12,13,14,15) + d(0)
D3D2
X |  |  | 
1 | 1 | 1 | 1
1 | 1 | 1 | 1
1 | 1 | 1 | 1
D1D0
00 01 11 10
D1
D2
D0
D3
00
01
11
10
D3D2
X |  | 1 | 1
1 | 1 | 1 | 1
1 | 1 | 1 | 1
D1D0
00 01 11 10
D1
D2
D0
D3
00
01
11
10
A1 = D2 + D3
A0 = D3 + D1D2’

## Slide 40
40
A1 = D2 + D3 A0 = D3 + D1D2’
Example: 4x2 Priority Encoder
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 41
41
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
Boolean Function Implementation using MSI Circuits

## Slide 42
42
Using 4:1 MUX design
AND gate
OR gate
NOT gate
Try it yourself
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
GND
+5v
AND
GND
+5v
OR
GND
+5v
NOT
X
X
A B
A B
A

## Slide 43
43
a)Build the following function using 8x1 Mux.
F(A,B,C)=∑(0,4,5)
b)Design same thing with 3x8 decoder
c) Try designing it with single 4x1 Mux
Try it yourself
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 44
44
F=∑(0,4,5)
Solution
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
5V
a)
b)

## Slide 45
45
If the two minterms in a column are not circled, apply 0 to the corresponding multiplexer input.
If the two minterms are circled, apply 1 to the corresponding multiplexer input.
If the bottom minterm is circled and the top is not circled, apply A to the corresponding multiplexer input.
If the top minterm is circled and the bottom is not circled, apply A' to the corresponding multiplexer input.
Rules: for using smaller mux to build larger equation
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 46
46
Solution
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
1 A 0 0
B C
1 A
0
0
Answer: Part ( c )

## Slide 47
47
Build the following function using 4x1 MUX
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
F(A,B,C) = ∑ ( 1, 3, 5, 6)

## Slide 48
48
Try it yourself
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
Implement the below function using a 8x1 Mux.
Implement the below function using a 4x16 decoder and OR gates
F(A,B,C,D) = ∑ ( 0,1,3,4,8,9,15)

## Slide 49
49
Solution
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
a.

## Slide 50
50
Home-task: Try it yourself
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
Using 2:1 MUX design
AND gate
OR gate
NOT gate
Solution: Try YOUTUBE

## Slide 51
51
4 variables with 4x1 Mux
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
F(A,B,C,D) = ∑ ( 1,3,4,11,12,13,14,15)
A | B | C | D | min
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 2
0 | 0 | 1 | 1 | 3
0 | 1 | 0 | 0 | 4
0 | 1 | 0 | 1 | 5
0 | 1 | 1 | 0 | 6
0 | 1 | 1 | 1 | 7
1 | 0 | 0 | 0 | 8
1 | 0 | 0 | 1 | 9
1 | 0 | 1 | 0 | 10
1 | 0 | 1 | 1 | 11
1 | 1 | 0 | 0 | 12
1 | 1 | 0 | 1 | 13
1 | 1 | 1 | 0 | 14
1 | 1 | 1 | 1 | 15
 | I0 | I1 | I2 | I3
A’B’ | 0 | 1 | 2 | 3
A’B | 4 | 5 | 6 | 7
AB’ | 8 | 9 | 10 | 11
AB | 12 | 13 | 14 | 15
 | B | A⊙B | AB | A+B’
https://www.youtube.com/watch?v=c8lhlAX2JMk

## Slide 52
52
Try it yourself
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
Implement the boolean function using two 4:1 MUX(s) and one 2:1 MUX.
F(A,B,C,D) = ∑ (0,1,4,5,9,14,15)

## Slide 53
53
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
Combining MSI to build Combinational Design Circuit

## Slide 54
54
Design a BCD to Excess 3 code converter using ‘4x16’ decoder and ‘16x4’ encoder
Exercise time!
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 55
55
Solution:
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 56
56
Design a full adder using ‘3x8’ decoder and ‘4x2’ encoder
Exercise time!
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 57
57
Solution
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
X | Y | Z | C | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 58
58
Design a 2-bit parallel adder where you have to use appropriate encoders and decoders to build the internal circuit.
Exercise time!
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 59
59
Solution
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
4
2
2
4

## Slide 60
60
Design a 7 person voting system using encoder(s) and decoder(s) and parallel adder(s). You can not use full adders. Meaning, for the inputs, you MUST use encoder(s) and decoder(s) as required.
Exercise time!
Department of Computer Science and Engineering
CSE260 - Digital Logic Design

## Slide 61
61
Solution
Department of Computer Science and Engineering
CSE260 - Digital Logic Design
4
2
2
4

## Slide 62
62
Design a 19 person voting system using encoder(s) and decoder(s) and parallel adder(s). You can not use full adders. Meaning, for the inputs, you MUST use encoder(s) and decoder(s) as required. Make sure your circuit is optimized.
Try Yourself!
Department of Computer Science and Engineering
CSE260 - Digital Logic Design